## Slide 1: Address Resolution Protocol
ARP

## Slide 2: ARP Request (op code 1)
192.168.2.12
mac12
Step 1: Broadcast to ff:ff:ff:ff:ff:ff
My mac addr is mac12*
I am 192.168.2.12
Where is 192.168.2.13?
192.168.2.13
mac13
* Note: Assume Mac12 is a 48 bit mac address

## Slide 3: ARP Request (op code 1)
192.168.2.12
Step 1: Broadcast to ff:ff:ff:ff:ff:ff
My mac addr is mac12
I am 192.168.2.12
Where is 192.168.2.13?
192.168.2.13
Step 2: Stores the fact
mac12 has 192.168.2.12
in its ARP table

## Slide 4: ARP Reply (opcode 2)
192.168.2.12
mac12
Step 3: Unicast to mac12
My mac addr is mac13
I am 192.168.2.13
192.168.2.13
mac13
Step 4:.12 Stores the fact mac13 has 192.168.2.13
in its ARP table
* Note: Assume Mac13 is also 48 bit mac address

## Slide 5: Ethernet Frame encapsulation
Ethernet Packet Structure (edited to remove many fields)
Frame 1 (Maximum 1532 bytes)
[Protocols in frame: eth:ip:udp:data]
Ethernet II, Src: 00:11:95:c0:45:15), Dst: ff:ff:ff:ff:ff:ff
Type: IP (0x0800)
Internet Protocol, Src: 10.10.10.90, Dst: 10.10.10.255
Protocol: UDP (0x11)
User Datagram Protocol, Src Port: cap (1026), Dst Port: 64512 (64512)
0000 09 2b 13 38 0d 01 00 71 00 00 00 00 00 00 00 00 .+.8...q........
0010 00 00 00 00 00 00 00 00 00 00 00 00 00 11 95 c0 ................
Payload
Ethernet
IP
Checksum
Type is
IPv4 (0x0800)

## Slide 6
Ethernet
ARP
Checksum
Type is
ARP (0x8060)

## Slide 7: ARP Protocol
HTYPE (16 bits): Specifies Ethernet

## Slide 8: ARP Protocol
PTYPE (16 bits): e.g. 0x0800 would mean looking for an IPv4 address

## Slide 9: ARP Protocol
Num bytes in
MAC Address

## Slide 10: ARP Protocol
Num bytes in
IP Address (4)
How does it know
that protocol is IP?

## Slide 11: ARP Protocol
OP code*.
1-request
2-reply
*If OP Code is 1 then Sender is the node looking for an IP/MAC binding.

## Slide 12: ARP Protocol
Sender mac addr
48 bits
(SHA)

## Slide 13: ARP Protocol
Sender IP addr
(SPA)
Note: An ARP Probe packet does not have this (i.e. No assign SPA). In that case the SPA field is all 0’s.

## Slide 14: ARP Protocol
Target mac addr
(THA)

## Slide 15: ARP Protocol
Target IP addr
(TPA)

## Slide 16: ARP Announcement Packets (Gratuitous ARP)
Hey everyone! My IP address is now xxx.xxx.xxx.xxx. (deal with it!)
This is accomplished one of two ways:
1. ARP Request with TPA=SPA and THA = 0 .
2. ARP Reply with TPA = SPA and THA=SHA.
Can be used when MAC address changes (i.e. New network card).
For load balancing across multiple NIC’s in a single machine.
For Zeroconf protocol for assignment of link-local (169) addresses.
Preferred Method
(but both are in the standard)

## Slide 17: Miscellaneous
ARP Stuffing - Used to force network attached devices (i.e. IP cameras) to accept a remotely assigned IP address to allow connection from your computer for configuration purposes.
arptables – an add-on to linux to allow filtering rules for ARP, like iptables.
ARP Proxy – A system to allow a machine to process and forward requests to, and on behalf of another machine. (very bad)

## Slide 18: ARP Table (Cache)
Sometimes referred to as a Cache because of its temporary (transitory) nature.
To see your arp table use “arp –a” (linux, MacOS, Windows). Is “show arp” in cisco.
Two designation for bindings: (1) Static – associations mac-> IP assigned automatically. (e.g. broadcast [i.e. 255.], multicast [e.g. 224., 239.]); and (2) Dynamic -> discovered through ARP requests and responses. May change over time. (i.e. your gateway/router).

## Slide 19: ARP Spoofing
Intentionally incorrect binding of IP & MAC for the purpose on intercepting traffic between two or more host.
Mitigation
Reliance on a traffic management systems to detect malicious ARP requests/replies (Very hard to manage).
Authentication, authorization, and accounting (AAA).
Dynamic ARP Inspection
DHCP Snooping

## Slide 20: DHCP (BOOTP)
Assigns IP addresses from a remote network management device (i.e. router)
An alternative to manually assigning IP’s.